## Slide 1
Oliver Yang
Jun 5，2018
More Than Just Cloud
System Memory QoS Challenge

## Slide 2
More Than Just Cloud
1. Background

## Slide 3
More Than Just Cloud
Service Consolidation & Co-location Practice
Goal: Increase data center hardware utilization
Idea: Consolidate multiple workloads with acceptable QoS loss
  Borg/Kubernetes, VMware DRS etc.
Challenge: Avoid contentions among multiple workloads
  Workload characterizations
    Resource model: Compute bound + IO bound
    Time sharing: Peak time + Off-peak time
  OS resource control & isolation features

## Slide 4
More Than Just Cloud
More Challenges In Webscale Data Center
Scale-out optimization at large scale
  Resource QoS classifications & scheduling
  Workload placements(Bin-packing) algorithm
  Dynamic distributed load balance & scheduling
Constantly varying load challenges from cloud native applications
  The synthetic test environment has poor coverage
  Many issues can be only found on real online environment
  Using statistics to determine the impact of a change
  Performance or resource characters could be totally changed after a time period
  Paper: Performance Analysis of Cloud Applications – NSDI 2018

## Slide 5
More Than Just Cloud
Co-location Jitters & Causes
HW Resource Contentions
Skewed Access Pattern
Queuing Delays
Background Activities
System performance jitters RCA (Root Cause Analysis) can be very challenge…
          Burst randomly
          In a very short period
          Reported/found very late
          Always postmortem analysis
          Without enough debug data
        Tradeoff between utilization and QoS
          Avoid jitters by resource isolations

## Slide 6
More Than Just Cloud
OS Resource Control & Isolation
  System wide optimizations
    Hardware & Software cooperate together
    Full stack optimizations
  3 major aspects
    Performance isolation
    Fault isolation
    Utilization Increase
  CPU: CAT, Cgroup, Noise Clean, Scheduler Optimization
Memory: MBM, MBA, Cgroup, Idle page tracking
  IO: Write back Cgroup, Low/Upper limit，
  Weight, File Level-Based IO Throttle
  Network: TC, HTB, Lockless Qdisc

## Slide 7
More Than Just Cloud
Why Memory Matters
  DRAM cost is close to CPU recently
  Memory is incompressible resource
  Challenges
    Capacity planning is difficult: OOM, Various Jitters, Bad utilization
    Memory overcommit has more risks: OOM, Jitter
    The bottlenecks of compute density
      Big data, Tensorflow…
      4 NUMA node servers
  Opportunities
    New NVM hardware
      AEP, Optane, NVME SSD
    AI technologies

## Slide 8
More Than Just Cloud
Memory QoS Requirements
  Performance Isolation
    Memory access performance shouldn’t be interfered by other containers/VMs.
  Fault Isolation
    Memory faults should be self-contained and shouldn’t have global QoS impacts
  Utilization Increase
    Memory utilization should be increased without QoS regressions
Fault Isolation
Software fault
Hardware fault
Utilization Increase
Capacity Planning
Memory Overcommit
Perf Isolation
Throughput
Latency

## Slide 9
More Than Just Cloud
2. Performance Isolation

## Slide 10
More Than Just Cloud
Performance Isolation - Direct Memory Access
Memory Performance
Direct Access
TLB
L1
L2
L1/L2/LLC
Local
Remote
DRAM
Local
Remote
Device MMIO
Paging on demand
Fast Path
Slow Path
Local
Remote
Problem: Hardware resource contention
Analysis: CPU PMU counters
Solution: Hardware & software work together
  Intel RDT (CAT/MBA)
  Software memory access pattern optimization
    TLB/Cache/Memory(NUMA)

## Slide 11
More Than Just Cloud
Perf Metrics For Direct Memory Access
CPI/IPC/MIPS
Perf stat - IPC
Pmu-tools – toplev, ocperf
TLB Hit/Miss/Flush
Perf stat – tlb miss, flush events
Cache Hit/Miss
Perf mem – access ratio
Memory Latency/BPS/IOPS
Numatop - Local/Rmote
Perf c2c – access ratio, latency
Perf c2c – access ratio, latency
Perf stat – cache miss events
Resctrl - CQM and MBM
perf mem – access ratio
Notes: Some metrics have performance overheads

## Slide 12
More Than Just Cloud
PMU Example 1 - IPC/Branch Miss/Cache Hit Profiling
PMU counters analysis based on perf stat
https://github.com/brendangregg/pmc-cloud-tools

## Slide 13
More Than Just Cloud
PMU Example 2 - Direct Memory Access Sampling
Using perf mem sampling
System wides & per-task

## Slide 14
More Than Just Cloud
Detecting Noisy Neighbors - CPI/IPC
CPI - Cycle Per Instruction
  IPC = 1 / CPI
  Paper - CPI2: CPU performance isolation for shared compute clusters, Eurosys 2013
Intel Top-down Microarchitecture Analysis Method
  PMU tools: https://github.com/andikleen/pmu-tools/wiki/toplev-manual

## Slide 15
More Than Just Cloud
Detecting Noisy Neighbors - CPI Flame Graph

## Slide 16
More Than Just Cloud
Case Study 1 - Contention Detection By CPI
Under sysbench & memory interference testing, MySQL TPS showed strong correlation with CPI
Notes: While MySQL TPS got dropped, the CPI was increased significantly

## Slide 17
More Than Just Cloud
Case Study 2 - Fix Skew Memory Access Pattern
Cache false sharing debug
  Using perf c2c
  Focus on HITM
  HITM - Hit In The Modified
  Perf Boost 17.96%

## Slide 18
More Than Just Cloud
Performance Isolation - On Demand Paging
Problem: Overheads from kernel paging mechanism
Analysis: Kernel counters and dynamic tracing
Solutions: Avoid running into slow path
  Warm up and lock the pages
  Increase min_free_kbytes vs. memory utilization
  Google patch: per-memcg kswapd (incomplete & need more enhancements)
Paging on demand
Fast Path
Buddy
Slow Path
Compact
Direct
Background
Reclaim
Direct
Loop & Yield
Sleep
Background
THP
Zero out
COW
Split
Collapse
Lock contention
Dirty
Congestion

## Slide 19
More Than Just Cloud
Memory Performance Isolation Challenges
Constantly varying load breaks static configurations
  Offline capacity planning is not accurate
  Static RDT (CAT/MBA) configurations can be broken
  Static cgroup upper limit, low limit, reclaim watermark can be broken
Too many slow path corner cases under low free memory conditions
  Memcg direct reclaim jitters under heavy buffer IO
  Memory fragmentation and compaction jitters for long uptime system
  THP (Transparent Huge Page) jitters under latency sensitive use cases
Online diagnosis, many jitters can only be found on real environment
  Couldn’t be reproduced in the local synthetic test environment
  Need continuous QoS data collecting and monitoring
  Need online full stack tracing
Lack of cluster range QoS data statistics
  Counter based metrics is not meaningful, and couldn’t be used for cluster statistic
  Fine granularity statistics, for example, cgroup, task levels

## Slide 20
More Than Just Cloud
Possible Solutions
Dynamic resource allocator for constantly varying load
  Real time resource conflicts detection
  Dynamic resource allocation for resilience handling
Avoid long-tail performance issue under low free memory conditions
  Smarter capacity planning, not only offline, but also online
  Smarter resource resource overcommit algorithm
Online & offline data collecting, diagnosis and prediction
  QoS data analysis in cluster range
  Jitter data collecting and diagnosis
  Semi-real time analysis and prediction

## Slide 21
More Than Just Cloud
Cluster QoS Data Normalization
Counter based metrics are not good for latency analysis
  TLB miss, Cache miss, Page fault, Alloc stall, Compact stall
Use time based metrics for cluster data normalization
  memdelay
    Translated delays from counters into a pressure percentage of lost wall time
  PSI - next version of memdelay
    Expand the ideas to cover pressure stall information for CPU, memory, and IO
Monitor interval (Wall Time)
memdelay by Johannes Weiner
Slow Path time

## Slide 22
More Than Just Cloud
Example 1: TLB Miss Data Normalization
Time based TLB miss analysis
7% TLB miss time in past 7 seconds

## Slide 23
More Than Just Cloud
Example 2: Direct Reclaim Data Normalization
Direct reclaim
  The allocstall counter in /proc/vmstat
  Direct reclaim tracepoints
  vmscan:mm_vmscan_direct_reclaim_begin vmscan:mm_vmscan_direct_reclaim_end
Direct reclaim latency histogram for a cluster
Latency range
Cumulative statistical data

## Slide 24
More Than Just Cloud
3. Fault Isolation

## Slide 25
More Than Just Cloud
Memory Faults & QoS Impacts
Software Fault
  OOM Handling
  Split-lock usage
  Segfault from application
Hardware Fault
  CE - Correctable Error
  UE - Uncorrectable Error
QoS impacts
  OS jitters caused by errors handling
  Memory access latency

## Slide 26
More Than Just Cloud
Fault Isolation Challenges
The significant interferences from faulty Cgroup
  Fault handling code
    Contention from global locks
    Priority Inversion
    TLB flush interrupts
    IO pressure caused by core dump
  Split-lock usage from buggy application
  Error interrupts triggered by hardware errors
    CMCI, NMI, SMI interrupts
OOM kill is NOT reliable, and has long latency
  Resource starving under cgroup OOM handling
Lack of cluster online/offline faults statistics
Difficult to predict memory faults

## Slide 27
More Than Just Cloud
Fault Handling Improvements
Cgroup OOM improvements
  Predictable OOM kill: OOM reaper
  Reduced overheads: OOM kill fixes
  Efficient OOM kill: cgroup aware OOM kill
Fill online/offline memory faults analysis gaps
  OOM counters: host and cgroup
  Split-locks monitoring
  Hardware faults monitoring
  Interrupts monitoring
  Memory faults VS. memory utilization, analysis together

## Slide 28
More Than Just Cloud
OOM Interferences - A Design Issue
A memcg design problem
  Memory pages are fully shared among Cgroups
  Global locking and data structure couldn’t be avoided
  Always could have jitters problems while cgroup OOM handling
Solutions
  Using RunV for better fault isolation.
  For RunC usage, the best way is to avoid OOM
    Accurate memory working set estimation
    A better memory starving prediction algorithm for memory overcommit

## Slide 29
More Than Just Cloud
Split Lock Isolation - HW & SW solution
Software bugs
  Atomic operation cross two cache lines
  Overall system performance got impacts by faulty application
Solutions
  Fix software bugs
  Detecting split-locks and control split locks
    #AC exception for new Intel processors
    PMU data analysis
  Fault isolation
    Some error handlings in #AC handlers
    Other ways…

## Slide 30
More Than Just Cloud
4. Utilization Increase

## Slide 31
More Than Just Cloud
Memory Utilization Increase Challenges
Memory utilization could be wrong, need to use memory working set
Rethinking memory working set
Formula | Comments
(Total - Free) / Total | Not good. There are lots of file read/write once cases.
(Total - Free – Inactive Cache) / Total | Not good. Cache could be still actively used.
(Memory Working Set) / Total | Sounds good. But how do you get the Working Set?
Paper: The Working Set Model for Program Behavior - ACM 1968
Working Sets Past and Present – IEEE 1980
Co-location: Memory reclaim always works.

## Slide 32
More Than Just Cloud
Memory Working Set Estimation
Use LRU inactive size
  Kubernetes: WS = Usage – Inactive Page Cache
Use Linux idle page tracking
  Kubernetes RFE: https://github.com/kubernetes/kubernetes/issues/12422
Source code：https://github.com/google/cadvisor/blob/master/container/libcontainer/handler.go#L519

## Slide 33
More Than Just Cloud
Linux Idle Page Tracking
Use Case
  Documentation/admin-guide/mm/idle_page_tracking.rst
  Estimate workload's working set size, so that…
    Setting memory cgroup upper limits for resource control
    Setting memory cgroup low limits for best efforts working set protection.
    Deciding where to place the workload within a compute cluster.
    Determine the effective memory utilization
Interfaces
  New: /sys/kernel/mm/page_idle/bitmap
  Cooperate existing kernel information
    Per-process: /proc/PID/pagemap
    Per-cgroup: /proc/kpagecgroup
    System wide: (0..MAX_PFN]
    Identify special pages: /proc/kpageflags

## Slide 34
More Than Just Cloud
Redefine Memory Utilization
Effective Memory Utilization
  No Swap: (Total - Free - Idle Page Cache) / Total
  With swap: (Total - Free - Idle Memory) / Total
Online capacity planning by effective memory utilization
  Online/offline data analysis from any clusters (thousand of machines)
  Understand spatial and time imbalance of memory resource

## Slide 35
Paper: Large-scale cluster management at Google with Borg - EuroSys 2015
More Than Just Cloud
Memory Reclamation & Challenges
Key idea:
  Find reusable memory for Best-Effort workload
  Kill Best Efforts workload proactively while memory contentions
  Challenges: Memory utilization & QoS tradeoffs
  Accurate working-set estimation for continuously-varying load
    To quickly find reusable memory resource
    To predict & detect memory starving accurately
Idle page tracking gives accurate working-set estimation

## Slide 36
More Than Just Cloud
5. Summary

## Slide 37
More Than Just Cloud
Recap
Memory performance isolation
  Using PMU counters for hardware resource contention detection
  Low free memory causes lots of OS Jitters, need a smarter way
  Using online cluster statistics for utilization and QoS tradeoff
Memory faults isolation
  Using RunV solution to meet higher QoS requirements
  For RunC, try to avoid/predict faults, such as OOM, split-lock, to overcome jitters
Memory utilization increase
  Capacity planning can be more accurate by using idle page tracking
  Continuously varying load requires online capacity planning
  Memory reclamation solution relies on accurate working-set estimation

## Slide 38
More Than Just Cloud
References
Linux Idle Page Tracking
Intel Top-down Microarchitecture Analysis Method
Brendan Gregg Blogs
  CPU utilization is wrong
  CPI flame graph
  How To Measure the Working Set Size on Linux
Resctrl UI
Perf C2C

## Slide 39
More Than Just Cloud
A TEAM OF EXPERTS
6000+ Top Technology Experts Based in Hangzhou, Beijing, Silicon Valley and Seattle.
MISSION
为了无法计算的价值
More Than Just Cloud
VISION
成为全球云数据大计算的领导者
Pioneer of Cloud Data and Big Computing
Alibaba Cloud